## Slide 1: Map Analysis and Modeling in Forestry’s Future: …where we are headed and how we can get there
Joseph K. Berry

## Slide 2
The lion’s share of GIS’s growth has been in ever expanding capabilities as a “technical tool” for corralling vast amounts of spatial data and providing near instantaneous access to remote sensing images, GPS navigation, interactive maps, asset management records, geo-queries and awesome displays. In just forty years GIS has morphed from boxes of cards passed through a window, to today’s sizzle of a 3D fly-through rendering of terrain anywhere in the world with back-dropped imagery and semi-transparent map layers draped on top—
all pushed from the cloud to a GPS enabled tablet or smart phone. What a ride!!!
Over 35 years of teaching graduate courses and professional workshops in grid-based map analysis and modeling has lead me
to believe that there is…
a “map-ematics” that extends traditional math/stat concepts and procedures for quantitative analysis of mapped data.
The premise is that “maps are numbers first, pictures later” and we do mathematical things to mapped data that moves GIS from
“Where is What” graphical inventories to a
“Why, So What and What If” problem solving environment—
“Thinking with Maps”
Making a Case for Map-ematics (analytical tool)
However, GIS as an “analytical tool” hasn’t experienced the same meteoric rise—
in fact it might be argued that the analytic side of GIS has
somewhat stalled over the last decade.

## Slide 3
The “-ists” and the “-ologists”
Together the “-ists” and the “-ologists” frame and develop the Solution for an application
The “-ists”
The “-ologists”
— and —
Why, So What, What If
Spatial Reasoning
Where is What
GIS Expertise
Technology
Experts
“-ists”
Domain
Experts
“-ologists”
Solution
Space
Application Space
Geotechnology’s Core
…understand the “science” behind spatial relationships that can be used for decision-making
Knowledge and Wisdom
focus
…understand the “tools” that can be used to display, query and analyze spatial data
Data and Information
focus

## Slide 4
The “-ists” and the “-ologists” (a bigger tent)
“Policy Makers”
…under Stakeholder, Policy & Public auspices
“Stakeholders”
Decision Makers utilize the Solution
“Decision Makers”
Technology
Experts
“-ists”
Domain
Experts
“-ologists”
Solution
Space
Application Space
Geotechnology’s Core
We are simultaneously trivializing…
…and complicating GIS Technology

## Slide 5
Spatial Analysis Operations (Geographic Context)
GIS as a “Technical Tool” (Where is What) vs. an “Analytical Tool” (Why, So What and What if)
GIS Perspective:
Reclassify (Position, Value, Size, Shape, Contiguity)
Overlay (Location-specific, Region-wide, Map-wide)
Distance (Distance, Proximity, Movement, Optimal Path, Visual Exposure)
Neighbors (Characterizing Surface Configuration, Summarizing Values)
Spatial Analysis
Map Stack
Grid Layer
Mathematical Perspective:
Map Analysis
Toolbox
Basic GridMath & Map Algebra ( + - * / )
Advanced GridMath (Math, Trig, Logical Functions)
Map Calculus (Spatial Derivative, Spatial Integral)
Map Geometry (Euclidian Proximity, Narrowness, Effective Proximity)
Plane Geometry Connectivity (Optimal Path, Optimal Path Density)
Solid Geometry Connectivity (Viewshed, Visual Exposure)
Unique Map Analytics (Contiguity, Size/Shape/Integrity, Masking, Profile)

## Slide 6
Spatial Analysis Operations (Math Examples)
y = fn(x)
The integral calculates the area under the curve for any section of a function.
Curve
Map Calculus — Spatial Derivative, Spatial Integral
Advanced Grid Math — Math, Trig, Logical Functions
Spatial Integral
Surface
COMPOSITE Districts WITH MapSurface Average FOR MapSurface_Davg
MapSurface Davg
…summarizes the values on a surface for specified map areas
(Total= volume under the surface)
Slope draped over
MapSurface
0%
65%
Spatial Derivative
…is equivalent to the slope of the tangent plane at a location
SLOPE MapSurface Fitted
FOR MapSurface_slope
Fitted Plane
Surface
500
2500
MapSurface
Advanced Grid Math
Surface Area
…increases with increasing inclination as a Trig function of the cosine of the
Slope Angle
SArea=
Fn(Slope)
Dzxy Elevation
ʃ Districts_Average Elevation
Curve
The derivative is the instantaneous “rate of change” of a function and is equivalent to the slope of the tangent line at a point

## Slide 7
 Counts
# Viewer cells
270/621= 43%
of the entire road network connected
“Visual
Exposure”
Roads
Highest
Exposure
Sums
Viewer
Weights 
Map Geometry — (Euclidian Proximity, Narrowness, Effective Proximity)
Plane Geometry Connectivity — (Optimal Path, Optimal Path Density)
Solid Geometry Connectivity — (Viewshed, Visual Exposure)
Spatial Analysis Operations (Distance Examples)
“Travel-Time”
Effective Proximity
…not necessarily straight lines (movement)
HQ (start)
On Road
26.5
minutes
…farthest away
by truck
Off Road
Absolute Barrier
On + Off
Road
96.0 minutes
…farthest away by truck, ATV and hiking
Off Road
Relative Barriers
Farthest
(end)
HQ
(start)
…the “steepest
downhill path”
identifies the
optimal route
(Quickest)
Seen if new tangent exceeds all previous tangents along the line of sight
Tan = Rise/Run
Rise
Run
Viewshed
“Splash”
Euclidean Proximity
…from a point to
everywhere…
“Splash”
Distance
Shortest straight line between two points…
Plane Geometry
Connectivity
Solid Geometry
Connectivity

## Slide 8
Spatial Statistics Operations (Numeric Context)
GIS as a “Technical Tool” (Where is What) vs. an “Analytical Tool” (Why, So What and What if)
Surface Modeling (Density Analysis, Spatial Interpolation, Map Generalization)
Spatial Data Mining (Descriptive, Predictive, Prescriptive)
GIS Perspective:
Spatial Statistics
Map Stack
Grid Layer
Basic Descriptive Statistics (Min, Max, Median, Mean, StDev, etc.)
Basic Classification (Reclassify, Contouring, Normalization)
Map Comparison (Joint Coincidence, Statistical Tests)
Unique Map Statistics (Roving Window and Regional Summaries)
Surface Modeling (Density Analysis, Spatial Interpolation)
Advanced Classification (Map Similarity, Maximum Likelihood, Clustering)
Predictive Statistics (Map Correlation/Regression, Data Mining Engines)
Statistical Perspective:
Map Analysis
Toolbox

## Slide 9
Histogram
70
60
50
40
30
20
10
0
80
In Geographic Space, the typical value forms a horizontal plane implying the average is everywhere
Geographic Distribution
X= 22.6
Spatial Statistics (Linking Data Space with Geographic Space)
Geo-registered Sample Data
Surface Modeling techniques are used to derive a continuous map surface from discrete point data– fits a Surface to the data.
Surface
Modeling
Continuous
Map Surface
Average = 22.6
StDev = 26.2
Standard Normal Curve
Non-Spatial Statistics
In Data Space, a standard normal curve can be fitted to data to identify the “typical value” (average)
Numeric Distribution
What
Spatial
Statistics
Roving Window (weighted average)
Discrete
Samplet Map
What
is
Where
+StDev
Average
…NE locations are “unusually” high
X + 1SD
= 48.8
StDev= 26.2

## Slide 10
r = .562 Localized
Spatial Statistics Operations (Data Mining Examples)
Elevation
(Feet)
Map Clustering:
Slope
(Percent)
Elevation
(Feet)
Slope
(Percent)
Map Correlation:
Roving
Window
Localized Correlation:
Map Variable – continuous quantitative surface represents the localized spatial relationship between the two map surfaces
… 81map values for
localized summary
= 625 small data tables within 5 cell reach per table
Scalar Value – one value represents the overall non-spatial relationship between the two map surfaces
Spatially Aggregated Correlation:
…where x = Elevation value and y = Slope value
and n = number of value pairs
r =
=1 large data table
with 25rows x 25 columns
= 625 map values for map wide summary
Entire Map
Slope draped
on Elevation
…relatively High,Steep
Elevation vs. Slope Scatterplot
Data Space
Elevation 
Slope 
Geographic Space
Cluster 1
Cluster 2
Cluster 3
Two Clusters
Three Clusters
Cluster 1
Cluster 2
…data pairs are grouped into
similar response patterns—
C1= Low, Low
C2= High, High
r = .432 Aggregated

## Slide 11
Banquet Table
“Stakeholders”
“Publics”
“Regulators”
“Policy-makers”
“Decision-makers”
Future Directions:
Podium
Historically Ecosystem Sustainability and Economic Viability have dominated Natural Resources discussion, policy and management.
The Softer Side of GIS (The NR Experience)
Social Acceptability
as 3rd filter/rail
Spatial Reasoning, Dialog and Consensus Building
Inter-disciplinary Science
Team Table
“-ists”
“-ologists”
Increasing Social Science & Diverse Involvement
1970s
2010s
But Social Acceptability has become the critical third filter needed for successful decision-making.

## Slide 12
So What’s the Point?
3) Grid-based map analysis and modeling involving Spatial Analysis and Spatial Statistics is in large part, simply extensions of traditional mathematics and
statistics concepts and procedures.
1) Current GIS education in NR for the most part insists that non-GIS students/professionals interested in understanding map analysis and modeling must be tracked into general GIS offerings that are primarily designed for GIS specialists, and that the material presented primarily focus on commercial GIS software mechanics that GIS-specialists need to know for the workplace.
4) Two paradigm shifts are needed— recognition by the GIS community that quantitative analysis of maps is a reality, and…
…recognition by the STEM community that spatial relationships exist and are quantifiable.
2) However, solutions to complex spatial problems need to engage “domain expertise” in GIS–
outreach to other disciplines to establish spatial reasoning skills needed for effective solutions that integrate a multitude of disciplinary and general public perspectives.
Handout
www.innovativegis.com/basis/Papers/Other/Esri_Forestry2012/

## Slide 13
Notes: Company branding slide